## Slide 1
WELL RISK ANALYSIS FOR THE
SAN JUAN BASIN CARBONSAFE PHASE III
by
Van Tang Nguyen
Department of Petroleum Engineering

## Slide 2: I. INTRODUCTION
International Energy Agency (IEA) 2023, CCUS Projects Database, IEA, Paris, http://www.iea.org/data-and-statistics/data-product/ccus-projects-database
Currently, the long-term Carbon Capture Utilization and Storage (CCUS) has received a lot of attention.
CO2 storage projects supported by the Department of Energy are underway across the country, San Juan Basin is one of the places for CO2 storage project
http://sccs.org.uk/resources/global-ccs-map
§146.84 Area of review and corrective action
“Owners or operators of Class VI wells must perform corrective action on all wells in the area of review that are determined to need corrective action”
Develop screening process to prioritize high risk wells
Notes: We could see from the chart that from 2020 until now, number of CCUS projects has been increase significantly. There is about 573 projects
There is around 162 projects which required transport, storage and T&S. In which, number of projects in US contribute to about 21 %
CCUS is hot projects and US also pay attention to this type of project

## Slide 3: II. WELL RISK
§ 146.94 Emergency and remedial response.
“The Director may allow the operator to resume injection prior to remediation if the owner or operator demonstrates that the injection operation will not endanger USDWs.”
§146.86 Injection well construction requirements.
“The owner or operator must ensure that all Class VI wells are constructed and completed to: (1) Prevent the movement of fluids into or between USDWs or into any unauthorized zones”
Well will be considered high-risk whenever it has chances of leakage or fluid immigrating to USDWs or unauthorized zones.
§ 146.88.a Injection well operating requirements.
“In no case may injection pressure initiate fractures in the confining zone(s) or cause the movement of injection or formation fluids that endangers a USDW”
Notes: The Screening process will apply Risk Assessment method to calculate Risk Score to choose high risk wells. The higher the risk score, the risker the well
The Risk Score is the product of Severity Score (SS) and the Weighting Factor (WF)

## Slide 4: III. RISK SCORE
  Applying Risk Assessment method to calculate Risk Score to choose high risk wells
  The Risk Score is the product of Severity Score (SS) and the Weighting Factor (WF)
Range (1 – 5)
Reflect the impact of the factor on wellbore integrity
11 factors
Weighting Factor
Severity Score
Range (1 – 5)
Reflect the severity of each category in each factor
Risk Score
Notes: The Screening process will apply Risk Assessment method to calculate Risk Score to choose high risk wells. The higher the risk score, the risker the well
The Risk Score is the product of Severity Score (SS) and the Weighting Factor (WF)

## Slide 5: III.1. Data Processing
Based on testing records collected in 3 states from (Greg Lackey et al, 2021)
Using ROC-AUC to choose the best algorithm for the data set
Apply feature importance for evaluating the effect of each factor on SCP and CVF

## Slide 6: III.2. Assigning Score
Injection reservoir
Cap rock
Reservoir
Reservoir
5
1
4
Reservoir
Reservoir
2
Well Status | SS
Plugged | 4
Inactive | 5
Active | 3
Abandoned | 1
Notes: It is important to consider the perforated reservoir because perforations are channels for fluid migration, especially in the class VI well area, where the injection reservoir will have high pressure due to the injection of CO2.

## Slide 7: III.3. Estimated leakage rate
Notes: According to On et al. (2022), changes in casing pressure can result in the formation of microannuli along the cement-casing interface, which can cause leaks.
To ensure that class VI wells are safe, it is crucial to estimate leakage caused by differential pressure. The model created by On et al. (2022) is also used in this work to determine the likely leakage rate.
Utilizing the Darcy formula presented in Eqs (2.10) and (2.11), the likely leakage rate in the bulk cement is calculated.
On et al. (2022) shows that differential pressure has impacts on permeability of cement,
On et al. (2022) also proved that differential pressure induces microannuli inside the cement which can cause leakage. The Figure show the distribution of microannuli sizes with applying of 1000-psi differential pressure.
Because of microannulus, leakage through cement annulus also should be considered and proposed to calculate as shown in the Equation

## Slide 8: III.4. Summary
No | FACTOR | DESCRIPTION |  | SS | WF
8 | Distance SCS to Water Table (ft) | Within WT; >5000 |  | 5 | 1
 |  | <50 |  | 4 | 
 |  | 50-2000 |  | 2 | 
 |  | 2000-5000 |  | 3 | 
9 | Distance from TVD to Water Table (ft) | >1000 |  | 5 | 1
 |  | 1000-3000 |  | 4 | 
 |  | 3000-5000 |  | 3 | 
 |  | 5000-10000 |  | 2 | 
 |  | >10000 |  | 1 | 
10 | Stimulation | Acidizing | 1 treatment | 1.1 | 2
 |  |  | 2 treatments | 1.2 | 
 |  |  | >2 treatments | 1.5 | 
 |  | Hydraulic fracturing | 1 treatment | 1.1 | 
 |  |  | 2 treatments | 1.2 | 
 |  |  | >2 treatments | 1.5 | 
 |  | Perforation | 1 perforation | 1.5 | 
 |  |  | >1 perforations | 2 | 
11 | Perforated Reservoir | Produced and injection reservoir are separated by a caprock or caprock is perforated with a shallow distance |  | 1 | 5
 |  | Caprock is perforated with a deep distance or; produced is separated from the injection reservoir by three others |  | 2 | 
 |  | Produced and injection reservoirs are seperated by two others |  | 3 | 
 |  | Produced and injection reservoirs are seperated by another reservoir |  | 4 | 
 |  | Produced reservoir is the same as the injection reservoir. |  | 5 | 
No. | FACTOR | DESCRIPTION | SS | WF
1 | Well Age | Before 1930, Unknow | 5 | 1
 |  | 1930-1950 | 4 | 
 |  | 1950-1970 | 3 | 
 |  | 1970-1990 | 2 | 
 |  | After 1990 | 1 | 
2 | Wellbore Trajectory | Unknow | 5 | 3
 |  | Horizontal | 4 | 
 |  | Slanted | 3 | 
 |  | Deviated | 2 | 
 |  | Vertical | 1 | 
3 | Well Type | Undetermined | 5 | 4
 |  | Gas, Disposal, Injection | 4 | 
 |  | Oil, dry hole, monitoring | 1 | 
4 | Well Status | Inactive, undetermined | 5 | 1
 |  | Plugged | 4 | 
 |  | Active | 3 | 
 |  | Abandoned | 1 | 
5 | Estimated leakage rate (m3/year) | >50 | 5 | 5
 |  | 10-50 | 4 | 
 |  | 5-10 | 3 | 
 |  | 1-5 | 2 | 
 |  | <1 | 1 | 
6 | Number of casings | 0 | 5 | 3
 |  | 1 | 4 | 
 |  | 2 | 3 | 
 |  | 3 | 2 | 
 |  | >3 | 1 | 
7 | Cement status | Any casings that do not have TOC reach to the surface plug | 5 | 5
 |  | Liners which have TOC below the previous casing shoe | 2 | 
 |  | Liners which have TOC above the previous casing shoe; or all casings have TOC reach to the surface plug | 1 | 
Notes: Well status
Estimated leakage rate
Number of casings

## Slide 9: IV. A CASE STUDY– Input Information
Well (i) | Well Age | Well bore Trajectory | Well Type | Well status | Probable Leakage | Number of casing | Cementing Status | Distance SCS to WT | Distance TVD to WT | Stimulation | Perforated Formation
1 | 2 | 1 | 4 | 3 | 2 | 1 | 5 | 5 | 2 | 2 | 5
2 | 1 | 1 | 4 | 3 | 3 | 1 | 5 | 5 | 2 | 2 | 5
3 | 1 | 1 | 5 | 3 | 4 | 2 | 5 | 3 | 2 | 3 | 4
4 | 2 | 1 | 4 | 1 | 4 | 1 | 5 | 5 | 2 | 2 | 5
5 | 1 | 1 | 4 | 1 | 4 | 3 | 1 | 3 | 2 | 2 | 1
6 | 2 | 1 | 4 | 1 | 4 | 1 | 1 | 3 | 2 | 2 | 5
… | … | … | … | … | … | … | … | … | … | … | …
35 | 1 | 1 | 4 | 3 | 5 | 2 | 1 | 4 | 2 | 2 | 1
36 | 1 | 1 | 4 | 1 | 2 | 1 | 5 | 3 | 2 | 2 | 5

## Slide 10: IV. A CASE STUDY - Results
SJB CarbonSAFE Strat Test #001
Supercritical plume gas CO2 gas of scenarios in 30 years- at Entrada injection Zone

## Slide 11: IV. CONCLUSION
The primary goals of this research are to develop a model for evaluating risk of wells in the AoR;
Risk Assessment method, big data analytics and leakage rate model are used to build a model for evaluating risk of wells in the area
Results shows that:
  Leakage rate, perforated formation, cement status and well type have high impacts;
  Wellbore trajectory, stimulation status and number of casings have medium impacts;
  Surface casing depth, well age, and well status have lowest influences
A case study on 36 wells on the AoR has been carried out.
This technology effectively reduces the number of wells that need to reevaluate, which results in cost savings and time efficiency.

## Slide 12
THANK YOU FOR YOUR ATTENTION