## Slide 1
Use of Fuzzy Analytical Hierarchy Process Coupled with Data Mining for Base Condition Assessment of NMDOT Culverts
C. Richardson and A. Romero*
Department of Civil & Environmental Engineering
*Accelerated MS Undergraduate

## Slide 2: Culvert Asset Management Plan (CAMP)
3 yr NMDOT Funded Project
  NMT & NMSU
NMT Principal Investigators
  Claudia Wilson
  Isabel Morris
  Wes Cook
  Clint Richardson

## Slide 3: Culvert Asset Management Plan (CAMP)
External Survey of State Maintained Culverts
  50,706 culverts logged using handheld Trimble TDC600 GPS and User Input Data Dictionary
  40 students employed over three summers
Primary Base Condition Assessment Focus
  Reinforced Concrete Pipe Culvert
  Concrete Box Culvert
  Corrugated Metal Pipe Culvert

## Slide 4: CAMP Survey Importance Attributes Structural and Non-structural Defects
* Deterioration of concrete: culvert interior/exterior, headwall, or wingwall, such as spalling, cracks, or exposed rebar/mesh.
** Channel condition to culvert inlet
 | RCP | CBC | CMP
A | Deterioration* | Deterioration* | Corrosion
B | Siltation | Siltation | Siltation
C | Channel** | Channel** | Channel**
D | Scour | Scour | Scour
E | Physical Damage | Physical Damage | Physical Damage

## Slide 5: Data Mining using Excel® “If” Statements
NMDOT
  Schema code
Preliminary Data Mining
  Material Type
    Concrete, metal, wood, plastic
  Concrete Shape
    Circular, arch, box, ellipse
  Selected Surveyed Attributes

## Slide 6: Rating Scale Examples: Silting & Scour
Siltation Survey | Scale
Clean or less than 10% | 1
10% to 30% silted | 2
30% to 60% silted | 3
60% to 90% silted | 4
Greater than 90% silted | 5
Scour Survey | Scale
Zero to less than 1 ft | 1
1 ft to less than 3 ft | 2
3 ft to less than 8 ft | 3
Greater than 8 ft | 4
Corrosion Scale: 1 to 4
CMP Physical Damage Scale: 1 to 4
RCP & CBC Damage Scale: 1 to 3
RCP & CBC Deterioration Scale: 1 to 3
Channel Condition Scale: 1 to 5

## Slide 7: AHP vs FAHP Overview*
AHP lacks the ability to deal with vagueness and uncertainty in subjective personal judgement through its single crisp value pairwise comparisons
FAHP allows the decision maker to express approximate or flexible preference using triangular fuzzy numbers (TFNs) to achieve a higher level of accuracy and consistency of judgement than AHP
Additionally, multiple experts may be integrated with FAHP to yield a synergistic aggregation of individual judgements based on a geometric mean of pair-wise comparison responses
*Multi-criteria Decision Making Algorithms

## Slide 8: FAHP with Experts
Pairwise Comparisons
  5 Attributes Require 10 Pairwise Comparisons
Multiple Experts
  NMDOT
  Drainage Consultants
  Potentially Neighboring State DOT

## Slide 9: Linguistic Importance Scale & Triangular Fuzzy Scale Used
1,1,2
1,2,3
2,3,4
3,4,5
4,5,6

## Slide 10: Triangular Fuzzy Scale
Chart: TNF Value
| 1 | 2 | 3
 | 0 | 1 | 0
 | 0 | 1 | 0
 | 0 | 1 | 0
 | 0 | 1 | 0
The overlap characterizes uncertainty of the responses within that numerical range
Attributes weights could be significantly different depending on the design of fuzzy membership functions; should preferably be lesser than 50%

## Slide 11: FAHP Template for 10 Pairwise Comparisons
 | Left Criteria is Greater Importance |  |  |  |  | Right Criteria is Greater Importance |  |  |  | 
 | 5 | 4 | 3 | 2 | 1 | 2 | 3 | 4 | 5 | 
A |  |  | X |  |  |  |  |  |  | B
A |  |  |  |  |  |  | X |  |  | C
A |  |  |  | X |  |  |  |  |  | D
A |  |  |  |  | X |  |  |  |  | E
B |  |  |  |  |  |  |  | X |  | C
B |  | X |  |  |  |  |  |  |  | D
B |  |  |  |  |  | X |  |  |  | E
C |  |  |  |  | X |  |  |  |  | D
C |  |  |  |  |  |  |  | X |  | E
D |  |  | X |  |  |  |  |  |  | E

## Slide 12: FAHP Steps
Individual Pairwise Comparisons
Integrated Fuzzy Comparison Matrix
Relative Weight Vector Evaluation using Eigenvalue
Aggregate Relative Weight to Crisp Attribute Weights
Consistency Check

## Slide 13: FAHP Weights District 5: Two Expert Raters
 | RCP |  |  | CBC |  |  | CMP |  | 
 | 1 | 2 | Comp | 1 | 2 | Comp | 1 | 2 | Comp
A | 0.142 | 0.069 | 0.099 | 0.049 | 0.171 | 0.100 | 0.157 | 0.336 | 0.234
B | 0.214 | 0.201 | 0.213 | 0.083 | 0.155 | 0.115 | 0.236 | 0.130 | 0.171
C | 0.287 | 0.372 | 0.335 | 0.288 | 0.415 | 0.372 | 0.274 | 0.228 | 0.251
D | 0.184 | 0.186 | 0.178 | 0.369 | 0.138 | 0.245 | 0.206 | 0.193 | 0.208
E | 0.172 | 0.171 | 0.175 | 0.211 | 0.121 | 0.168 | 0.127 | 0.113 | 0.135
CR* | 0.046 | 0.035 | 0.023 | 0.104 | 0.000 | 0.025 | 0.191 | 0.201 | 0.086
*Consistency ratio (CR) is an important indicator for achieving the reliability of pairwise comparisons and should be less than 0.10.

## Slide 14: Inter-Rater Agreement Coefficient
Double Entropy Method
  Spread of responses and frequency distribution of responses
  Perfect agreement on a pairwise comparison 1.0
  No agreement on a pairwise comparison 0.0
  Inter-rater agreement coefficients in the range 0.6 to 0.7 may be considered as a reasonable cutoff for consensus, while values from 0 to 0.6 should be considered as unacceptable levels of agreement (Olenko and Tsyganok, 2016).

## Slide 15: Inter-rater Agreement District 5: Two Raters*
*Double Entropy Inter-rater Agreement Coefficient.
Pair-Wise Comparison | RCP | CBC | CMP
1 A to B | 0.78 | 0.78 | 0.05
2 A to C | 0.78 | 0.51 | 0.16
3 A to D | 0.51 | 0.16 | 0.78
4 A to E | 0.78 | 0.31 | 1.00
5 B to C | 0.78 | 0.78 | 0.78
6 B to D | 1.00 | 0.31 | 0.78
7 B to E | 1.00 | 0.31 | 1.00
8 C to D | 0.51 | 0.05 | 0.51
9 C to E | 0.78 | 1.00 | 0.51
10 D to E | 0.78 | 0.51 | 0.78

## Slide 16: Inter-rater Agreement District 5: Two Raters*
*A low COV means good agreement among decision makers on each criterion; or the extent of variability in relation to the mean of the judgments of the decision makers.
 | RCP | CBC | CMP
Average | 0.77 | 0.47 | 0.64
Stdev | 0.16 | 0.30 | 0.32
COV | 21.28 | 64.17 | 51.15

## Slide 17: Base Condition Assessment CMP: District 1
Culvert ID | Silting | Corrosion | Scour | Damage | Channel | Base
10773 | 1 | 1 | 2 | 1 | 1 | 1.25
10675 | 1 | 1 | 1 | 1 | 4 | 1.40
10684 | 1 | 3 | 1 | 1 | 1 | 1.47
10703 | 1 | 2 | 2 | 1 | 1 | 1.48
10707 | 1 | 2 | 3 | 1 | 1 | 1.74
10673 | 3 | 1 | 1 | 1 | 4 | 1.75
10744 | 1 | 2 | 1 | 2 | 4 | 1.85
10712 | 1 | 2 | 1 | 4 | 1 | 1.86
10700 | 2 | 3 | 2 | 1 | 1 | 1.89
10846 | 1 | 3 | 3 | 2 | 1 | 2.18
10856 | 4 | 4 | 1 | 2 | 1 | 2.42
10855 | 3 | 4 | 1 | 4 | 1 | 2.67